## Slide 1: Lecture : Kinematics:
Forward and Inverse Kinematics
Kinematic Chains

## Slide 2: Lecture 4: Kinematics:
Forward and Inverse Kinematics
Kinematic Chains
The Denavit-Hartenberg Convention

## Slide 3: Lecture 4: Kinematics:
Forward and Inverse Kinematics
Kinematic Chains
The Denavit-Hartenberg Convention
Inverse Kinematics

## Slide 4: Kinematic Chains
Basic Assumptions and Terminology:
A robot manipulator is composed of a set of links connected together by joints;

## Slide 5: Kinematic Chains
Basic Assumptions and Terminology:
•
A robot manipulator is composed of a set of links connected together by joints;
Joints can be either
◦
◦
◦
revolute joint (a rotation by an angle about fixed axis) prismatic joint (a displacement along a single axis)
more complicated joints (of 2 or 3 degrees of freedom) are represented as combinations of the simplest ones

## Slide 6: Kinematic Chains
Basic Assumptions and Terminology:
•
A robot manipulator is composed of a set of links connected together by joints;
Joints can be either
◦
◦
◦
revolute joint (a rotation by an angle about fixed axis) prismatic joint (a displacement along a single axis)
more complicated joints (of 2 or 3 degrees of freedom) are represented as combinations of the simplest ones
•
A robot manipulator with n joints will have (n + 1) links. Each joint connects two links;

## Slide 7: Kinematic Chains
Basic Assumptions and Terminology:
•
A robot manipulator is composed of a set of links connected together by joints;
Joints can be either
◦
◦
◦
revolute joint (a rotation by an angle about fixed axis) prismatic joint (a displacement along a single axis)
more complicated joints (of 2 or 3 degrees of freedom) are represented as combinations of the simplest ones
•
•
A robot manipulator with n joints will have (n + 1) links. Each joint connects two links;
We number joints from 1 to n, and links from 0 to n. So that joint i connects links (i − 1) and i;

## Slide 8: Kinematic Chains
Basic Assumptions and Terminology:
•
A robot manipulator is composed of a set of links connected together by joints;
Joints can be either
◦
◦
◦
revolute joint (a rotation by an angle about fixed axis) prismatic joint (a displacement along a single axis)
more complicated joints (of 2 or 3 degrees of freedom) are represented as combinations of the simplest ones
•
•
•
A robot manipulator with n joints will have (n + 1) links. Each joint connects two links;
We number joints from 1 to n, and links from 0 to n. So that joint i connects links (i − 1) and i;
The location of joint i is fixed with respect to the link (i − 1);

## Slide 9: Kinematic Chains
Basic Assumptions and Terminology:
When joint i is actuated, the link i moves. Hence the link 0
is fixed;

## Slide 10: Kinematic Chains
Basic Assumptions and Terminology:
•
When joint i is actuated, the link i moves. Hence the link 0
is fixed;
With the ith joint, we associate joint variable
i
q =



i
θ if joint i is revolute
di if joint i is prismatic

## Slide 11: Kinematic Chains
Basic Assumptions and Terminology:
•
When joint i is actuated, the link i moves. Hence the link 0
is fixed;
With the ith joint, we associate joint variable
i
q =



i
θ if joint i is revolute
di if joint i is prismatic
•
For each link we attached rigidly the coordinate frame,
oixiyizi for the link i;

## Slide 12: Kinematic Chains
Basic Assumptions and Terminology:
•
When joint i is actuated, the link i moves. Hence the link 0
is fixed;
With the ith joint, we associate joint variable
i
q =



i
θ if joint i is revolute
di if joint i is prismatic
•
•
For each link we attached rigidly the coordinate frame,
oixiyizi for the link i;
When joint i is actuated, the link i and its frame experience a motion;

## Slide 13: Kinematic Chains
Basic Assumptions and Terminology:
•
When joint i is actuated, the link i moves. Hence the link 0
is fixed;
With the ith joint, we associate joint variable
i
q =



i
θ if joint i is revolute
di if joint i is prismatic
•
•
•
For each link we attached rigidly the coordinate frame,
oixiyizi for the link i;
When joint i is actuated, the link i and its frame experience a motion;
The frame o0x0y0z0 attached to the base is referred to as inertia frame

## Slide 14: Kinematic Chains
Coordinate frames attached to elbow manipulator

## Slide 15: Kinematic Chains
Basic Assumptions and Terminology:
Suppose Ai is the homogeneous transformation that gives
◦
◦
position orientation
of frame oixiyizi with respect to frame oi−1xi−1yi−1zi−1;

## Slide 16: Kinematic Chains
Basic Assumptions and Terminology:
Suppose Ai is the homogeneous transformation that gives
◦
◦
position orientation
•
of frame oixiyizi with respect to frame oi−1xi−1yi−1zi−1; The matrix Ai is changing as robot configuration changes;

## Slide 17: Kinematic Chains
Basic Assumptions and Terminology:
Suppose Ai is the homogeneous transformation that gives
◦
◦
position orientation
•
•
of frame oixiyizi with respect to frame oi−1xi−1yi−1zi−1; The matrix Ai is changing as robot configuration changes;
Due to the assumptions Ai = Ai(qi), i.e. it is the function of a scalar variable;

## Slide 18: Kinematic Chains
Basic Assumptions and Terminology:
Suppose Ai is the homogeneous transformation that gives
◦
◦
position orientation
•
•
•
of frame oixiyizi with respect to frame oi−1xi−1yi−1zi−1; The matrix Ai is changing as robot configuration changes;
Due to the assumptions Ai = Ai(qi), i.e. it is the function of a scalar variable;
Homogeneous transformation that expresses the position and orientation of ojxjyjzj with respect to oixiyizi
T
i
j
=
.
Ai+1Ai+2 · · · Aj−1Aj,
I,
if i < j
if i = j
, Ti = (Tj)−1, if i > j
j i
is called a transformation matrix

## Slide 19: Kinematic Chains
If the position and orientation of the end-effector with respect to the inertia frame are
o0 ,
R0
n n
Then the position and orientation of the end-effector in inertia frame are given by homogeneous transformation
n
1 1 2 2
T 0 = A (q )A (q ) · · · An−1(qn−1)An(qn) =
Σ
R0 0
n o
n
0 1
Σ
with
i i
A (q ) =
R
oi
i−1 i−1 i
0
1
Σ Σ

## Slide 20: Kinematic Chains
If the position and orientation of the end-effector with respect to the inertia frame are
o0 ,
R0
n n
Then the position and orientation of the end-effector in inertia frame are given by homogeneous transformation
n
1 1 2 2
T 0 = A (q )A (q ) · · · An−1(qn−1)An(qn) =
Σ
R0 0
n o
n
0 1
Σ
with
i i
A (q ) =
R
oi
i−1 i−1 i
0
1
Σ Σ
i
⇒ Tj
= Ai+1Ai+2
· · · A
j−1Aj =
Σ
Ri i
j o
j
0 1
Σ
with
Ri
j
= Ri
i+1
j
· · · Rj−1,
oi
j
j−1
= oi + Ri
oj
j−1 j−1

## Slide 21: Lecture 4: Kinematics:
Forward and Inverse Kinematics
Kinematic Chains
The Denavit-Hartenberg Convention
Inverse Kinematics

## Slide 22: DH Convention:
The idea is to represent each homogeneous transform Ai as a product
Ai = Rotz,θi ·Transz,di ·Transx,ai ·Rotx,αi

θ
i
c −sθi
s
= θ

i
c
θi
0
0
 


i




i



0
α
i
α
i
s
α
i
c
α
i
0 0 1 0 0 0 1 0 0 a 1 0 0
0 0 0 1 0 0 0 1 0 0 0 c −s 0
0 1 0 0 0 1 d 0 0 1 0 0 0
0 0 1 0 0 0 1 0 0 0 1 0 0
0
1




## Slide 23: DH Convention:
The idea is to represent each homogeneous transform Ai as a product
Ai = Rotz,θi ·Transz,di ·Transx,ai ·Rotx,αi

θ
i
c −sθi
s
= θ

i
c
θi
0
0
 


i




i



0
α
i
α
i
s
α
i
c
α
i
0 0 1 0 0 0 1 0 0 a 1 0 0
0 0 0 1 0 0 0 1 0 0 0 c −s 0
0 1 0 0 0 1 d 0 0 1 0 0 0
0 0 1 0 0 0 1 0 0 0 1 0 0
0
1



The parameters of transform are known as
•
•
•
•
ai: link length αi: link twist di: link offset θi: link angle

## Slide 24: Conditions for Existence 4 Parameters:
DH1: The axis x1 is perpendicular to the axis z0
DH2: The axis x1 intersects the axis z0

## Slide 25: Assigning Frames Following DH-Convention:
Given a robot manipulator with
•
n revolute and/or prismatic joints
(n + 1) links
The task is to define coordinate frames for each link so that transformations between frames can be written in
DH-convention

## Slide 26: Assigning Frames Following DH-Convention:
Given a robot manipulator with
•
n revolute and/or prismatic joints
(n + 1) links
The task is to define coordinate frames for each link so that transformations between frames can be written in
DH-convention
The algorithm of assigning (n + 1) frames for (n + 1) links
treats separately first n-frames and the last one (end-effector frame)
is recursive in first part, so that it is generic

## Slide 27: Assigning First n-Frames
Step 1 (Choice of z-axises):
Choose z0-axis along the actuation line of the 1st-link;

## Slide 28: Assigning First n-Frames
Step 1 (Choice of z-axises):
Choose z0-axis along the actuation line of the 1st-link;
Choose z1-axis along the actuation line of the 2nd-link;

## Slide 29: Assigning First n-Frames
Step 1 (Choice of z-axises):
•
•
•
Choose z0-axis along the actuation line of the 1st-link; Choose z1-axis along the actuation line of the 2nd-link;
. . .
Choose z(n−1)-axis along the actuation line of the nth-link

## Slide 30: Assigning First n-Frames
Step 1 (Choice of z-axises):
•
•
•
Choose z0-axis along the actuation line of the 1st-link; Choose z1-axis along the actuation line of the 2nd-link;
. . .
Choose z(n−1)-axis along the actuation line of the nth-link
We need to finish the job and assign
•
•
point on each of zi-axis that will be the origin of the
ith-frame
xi-axis for each frame so that two DH-conditions hold
DH1: The axis x1 is perpendicular to the axis z0
DH2: The axis x1 intersects the axis z0 yi-axis for each frame

## Slide 31: Assigning First n-Frames
Step 2 (Choice of x-axises):
Suppose that we have chosen the (i − 1)th-frame and need to proceed with the ith-frame

## Slide 32: Assigning First n-Frames
Step 2 (Choice of x-axises):
•
Suppose that we have chosen the (i − 1)th-frame and need to proceed with the ith-frame
For the ith-frame, the zi axis is already fixed

## Slide 33: Assigning First n-Frames
Step 2 (Choice of x-axises):
•
•
Suppose that we have chosen the (i − 1)th-frame and need to proceed with the ith-frame
For the ith-frame, the zi axis is already fixed To meet conditions DH1-DH2
the xi-axis should intersects zi−1 and xi⊥zi−1 and xi⊥zi. Is it possible?

## Slide 34: Assigning First n-Frames
Step 2 (Choice of x-axises):
•
•
•
Suppose that we have chosen the (i − 1)th-frame and need to proceed with the ith-frame
For the ith-frame, the zi axis is already fixed To meet conditions DH1-DH2
the xi-axis should intersects zi−1 and xi⊥zi−1 and xi⊥zi. Is it possible?
There are 3 cases:
◦
◦
zi and zi−1 are not coplanar
zi and zi−1 are parallel
zi and zi−1 intersect

## Slide 35: Assigning First n-Frames
Step 2 (Choice of x-axises):
•
•
•
Suppose that we have chosen the (i − 1)th-frame and need to proceed with the ith-frame
For the ith-frame, the zi axis is already fixed To meet conditions DH1-DH2
the xi-axis should intersects zi−1 and xi⊥zi−1 and xi⊥zi. Is it possible?
There are 3 cases:
◦
◦
zi and zi−1 are not coplanar
zi and zi−1 are parallel
zi and zi−1 intersect
•
For all 3 cases it is possible!

## Slide 36: Assigning First n-Frames
Step 2 (Choice of x-axises):
If zi and zi−1 are not coplanar, then there is the common perpendicular for both lines!

## Slide 37: Assigning First n-Frames
Step 2 (Choice of x-axises):
If zi and zi−1 are not coplanar, then there is the common perpendicular for both lines!
It will define new origin oi and the xi-axis for the ith-frame

## Slide 38: Assigning First n-Frames
Step 2 (Choice of x-axises):
If zi and zi−1 are not coplanar, then there is the common perpendicular for both lines!
It will define new origin oi and the xi-axis for the ith-frame
If zi and zi−1 are parallel, then there are many common perpendiculars for both lines!

## Slide 39: Assigning First n-Frames
Step 2 (Choice of x-axises):
If zi and zi−1 are not coplanar, then there is the common perpendicular for both lines!
It will define new origin oi and the xi-axis for the ith-frame
If zi and zi−1 are parallel, then there are many common perpendiculars for both lines!
One of them will define new origin oi and the xi-axis for the
ith-frame

## Slide 40: Assigning First n-Frames
Step 2 (Choice of x-axises):
If zi and zi−1 are not coplanar, then there is the common perpendicular for both lines!
It will define new origin oi and the xi-axis for the ith-frame
If zi and zi−1 are parallel, then there are many common perpendiculars for both lines!
One of them will define new origin oi and the xi-axis for the
ith-frame
If zi and zi−1 intersect, then there is a vector orthogonal to the plane formed by zi and zi−1!

## Slide 41: Assigning First n-Frames
Step 2 (Choice of x-axises):
If zi and zi−1 are not coplanar, then there is the common perpendicular for both lines!
It will define new origin oi and the xi-axis for the ith-frame
If zi and zi−1 are parallel, then there are many common perpendiculars for both lines!
One of them will define new origin oi and the xi-axis for the
ith-frame
If zi and zi−1 intersect, then there is a vector orthogonal to the plane formed by zi and zi−1!
The point of intersection can be new origin oi and the xi-axis for the ith-frame is the orthogonal to this plane

## Slide 42: Assigning First n-Frames
Step 3 (Choice of y-axises):
If we have already chosen the vectors zi, xi and the point oi for the ith-frame, yi can be assigned by

## Slide 43: Assigning First n-Frames
Step 3 (Choice of y-axises):
If we have already chosen the vectors zi, xi and the point oi for the ith-frame, yi can be assigned by
cross-product operation: y˙i = z˙i × x˙i

## Slide 44
Illustration of DH-frame assignment

## Slide 45: Assigning the Last Frame for the End-Effector
For most robots zn−1 and zn coincide. So that the transformation between two frames is
•
•
translation by dn along zn−1-axis rotation by θn about zn-axis

## Slide 46
Example 3.1: Planar two-link manipulator

## Slide 47
Example 3.2: Three-link cylindrical manipulator