## Slide 1: Radon Transform
Section 2
Unit 4

## Slide 2: Introduction
The Radon transform is named after the Austrian mathematician Johann Karl August Radon (December 16, 1887 – May 25, 1956) .
The Radon transform is a remarkably versatile tool that finds application in many areas of medicine and applied physics.
The Radon transform is widely applicable to tomography, the creation of an image from the scattering data associated to cross-sectional scans of an object
The Radon transform data is often called a sinogram

## Slide 3: Introduction cont’d
In two dimensions (2D), the Radon transform is the set of all line-integral projections of a 2D function f(r).
For example, line integrals of the x-ray attenuation coefficient are obtained in computed tomography by passing a pencil beam of x-rays through a section of the body.
In single-photon emission computed tomography (SPECT), a parallel-hole collimator defines a pencil-like region of the body, so again line integrals are obtained, this time of the activity distribution.
And in positron-emission tomography (PET), coincident detection of two annihilation gamma rays defines a line through the body, and line integrals of the positron activity are measured.
The Radon transform in 3D refers to integrals over planes rather than lines. Plane integrals occur in some kinds of magnetic resonance imaging and in nuclear medicine if a slat collimator is used.

## Slide 4: Radon Transform
The 1D projection of a 2D function f(x,y), with the projection being defined by line integrals along a series of lines parallel to the y axis
The projection along the line x=ρ, denoted λθ(ρ), is given by

## Slide 5: Radon Transform
A more general projection is along the line ρ = r*n. In this case the projection is given by
where the integral runs over the infinite plane, and φ is the angle between the x axis and the unit vector n

## Slide 6: Radon Transform
The projection λθ(p), can be regarded either as a 1D function of ρ, parameterized by θ, or as a function in a 2D space with polar coordinates p and θ
The scalar ρ is thus the magnitude of the vector ρ, and θ is its polar angle relative to the x axis

## Slide 7: Radon Transform
Applying the Radon transform on an image f(x,y) for a given set of angles can be thought of as computing the projection of the image along the given angles
The resulting projection is the sum of the intensities of the pixels in each direction, i.e. a line integral.
The result is a new image R(p,φ).

## Slide 8: Radon Transform
This can be written mathematically by defining
ρ = x cosθ+ ysinθ
after which the Radon transform can be written as

## Slide 9: Radon Transform Principles
A linear transform f(x,y)  R(p,)
  Line integral or “ray-sum”
  Along a line inclined at angle  from y-axis and s away from origin
Fix  to get a 1-D signal R(s)
(From Jain’s Fig.10.2)
We have now a set of images R(s) which represent R(p,)
This is a transform from 2D to 2D spaces

## Slide 10: Computed Tomography Example

## Slide 12: Radon Transform and CT

## Slide 13: Example

## Slide 14: Example

## Slide 15: Example

## Slide 16: Example

## Slide 17: Example

## Slide 18: Example

## Slide 19: Example

## Slide 20: Full circle in RT

## Slide 21: Empty circle in RT

## Slide 22: RT of circle: Example

## Slide 23: RT of circle: Example

## Slide 24: RT of circle: Example

## Slide 25
RADON TRANSFORM Properties
REMEMBER: f(x,y)  p(r,)

## Slide 26: Properties

## Slide 27: Radon transform properties
Image of any f + g is F + G
Image of cf is cF for any real c
Rotation of f causes translation of F in α
Scaling of f in (x,y) causes scaling of F in s
Image of a point (2D Dirac function) is sine wave line

## Slide 28: Radon transform properties
6. Image of n points is a set of n sine wave lines
7. Image of a line is a point (2D Dirac function)
8. Image of polygon contour is a point set

## Slide 29: Inverse Radon Transform
Inverse Radon Transform

## Slide 30: Application of Radon Transform Example

## Slide 31: Reconstruction with more Rays

## Slide 32
Backpropagation
Principles

## Slide 33
Backpropagation
We know that objects are somewhere here in black stripes, but where?

## Slide 35: Example of Simple Backprojection Reconstruction
Given are sums, we have to reconstruct values of pixels A, B, C and D

## Slide 36
ART
Image Reconstruction: ART or Algebraic Reconstruction Technique

## Slide 37: Backprojection of Radon Transform

## Slide 39
Crisp edges
Blurred edges
Filtered backpropagation creates crisp edges
Ideal cylinder

## Slide 40: Radon transform back propagation in different directions

## Slide 41
Radon Transform - Reconstruction

## Slide 42: Reconstruction from 32 angles

## Slide 43: Reconstruction from 64 angles

## Slide 44: Reconstruction from 96 angles

## Slide 45: Reconstruction from 128 angles

## Slide 46: Reconstruction from 180 angles

## Slide 47: Reconstruction from 256 angles

## Slide 48: Reconstruction from 360 angles

## Slide 49: Reconstruction from 512 angles